## Slide 1
The History of the
Home Computer
– Part 1
“The 1977 Trinity”

## Slide 2
The History of the
Home Computer
– Part 1
“The 1977 Trinity”

## Slide 3
“The 1977 Trinity”

## Slide 4
“The 1977 Trinity”
Notes: Announced January, shipped October

## Slide 5
“The 1977 Trinity”

## Slide 6: A little bit about me…

## Slide 7: 2003
Notes: Compaq Deskpro
Omni 3
Anonymous beige boxes

## Slide 8: 2013
Notes: Compaq Deskpro
Omni 3
Anonymous beige boxes

## Slide 9: 1975 – MITS Altair 8800
Notes: Micro Instrumentation and Telemetry Systems (MITS)
Introduced:January 1975, Available:February 1975
Prices:US $395 as a kit(prior to March)US $650 assembled
How many:estimated 2000+
CPU:Intel 8080, 2.0 MHz RAM:256 bytes, 64K max Display:front panel LEDs Controls:front panel switches
Expansion:Altair-bus card-cage Storage:paper tape, cassette orfloppy drive
OS:CP/M, BASIC
First Computer which Bill Gates & Paul Allen wrote commercial software

## Slide 10: 1975 – MITS Altair 8800
Intel 8080 CPU
256 Bytes Memory
Front Panel Switches
“Blinkenlichten!”
Basic on paper tape
Notes: Micro Instrumentation and Telemetry Systems (MITS)
Introduced:January 1975, Available:February 1975
Prices:US $395 as a kit(prior to March)US $650 assembled
How many:estimated 2000+
CPU:Intel 8080, 2.0 MHz RAM:256 bytes, 64K max Display:front panel LEDs Controls:front panel switches
Expansion:Altair-bus card-cage Storage:paper tape, cassette orfloppy drive
OS:CP/M, BASIC
First Computer which Bill Gates & Paul Allen wrote commercial software

## Slide 11: 1985 -
Notes: Ship Date:July 1985
Price:US $1295 without monitorUS $1790 with RGB monitor
CPU:Motorola 68000 @ 7.14 MHz
RAM:256K stock, 512 typical - 8Meg max.
Display:16 colors at 640 X 400, 4096 colors at 320 X 200
Ports:Parallel, serial, floppy, RGB, RF, composite videoStereo audio, joysticks, System bus
Storage:Internal 880K 3.5-inch floppy.
OS:AmigaDOS 1.0-1.34"Workbench" GUI

## Slide 12: Driving the Revolution (1) - Memory
Early mechanical memories
  The Williams-Kilburn Tube
  Delay Line Memory
  Drum Memory

## Slide 13: Driving the Revolution (1) - Memory
Magnetic Core Memory - 1951
Notes: 1024 bits – 32 x 32, made by hand

## Slide 14: Driving the Revolution (1) - Memory
Semiconductor Memory – Static RAM
Intel started in 1968
Targeted market of LSI technology
Intel 3101
  1969, first successful product
  64 bit Static RAM
Intel 1101
  Late 1969
  256-bit Static RAM
  First use of MOS for RAM
  First high volume semiconductor RAM
Notes: http://www.cpu-zone.com/RAM_History.htm
1024 bits – 32 x 32, made by hand

## Slide 15: Driving the Revolution (1) - Memory
Disadvantages of Static RAM
Dynamic RAM (DRAM)
  Simpler to build
  Higher Densities
  Controlling it is more difficult
Intel 1103
  First commercial DRAM
  October 1970
  1024 x 1 bits
  By 1972, largest selling semiconductor
MOSTEK MK4096
  First multiplexed DRAM, 1973
  4096 x 1
Followed by MK4116
  1976
  16k x 1
  75% DRAM Market by end of 1979
Notes: 1024 bits – 32 x 32, made by hand

## Slide 16
Driving the Revolution (2) – Microprocessors
During 1960’s CPU consisted of 10’s -> 100’s discrete transistors.
Microprocessor integrates into a single piece of silicon, i.e. Integrated Circuit
Notes: CADC – U.S. – avionics control for the F14 Tomcat - ??? Secret until 1998 - Ray Holt
4004 – first commercial, used for calculators – 2,300 transistors, 0.1 mhz

## Slide 17
Driving the Revolution (2) – Microprocessors
CADC
Intel 4004
Intel 8008
Intel 8080
Zilog Z80
Motorola 6800
Notes: CADC – Central Air Data Computer – 1968 -> 1970 - Avionics control for the F14 Tomcat - Secret until 1998 - Ray Holt
Intel 4004 – 4 bit – 1971 - first commercial $60, used for calculators – 2,300 transistors, 0.1 - 0.7 mhz
Intel 8008 – early 8 bit – 1972 - $120 –
Intel 8080 – 2nd intel 8-bit – 1974 - $360 - 16-bit address bus, 64k ram – Blinkin Lights & CP/M - machines – 2 -3 mhz – CISC long instructutions – up to 11 cycles – Andy Grove, Robert Noyce and Gordon Moore – Rubylith
Zilog Z80 – Federico Fagin left after 8080 – founded Zilog 1974 – binary compatible –(CPM) simpler architecture – TRS80, sinclair zx-80, spectrum) – still used today in embedded systems
Motorola 6800 – 8-bit, 16-bit address bus – 1974 - $360 single unit - family of support chips (cpu, ram, rom, pia) – design team left…

## Slide 18: 6502
Notes: cheap Microprocessor, Motorola not interested
6800 team - Peddle - joined MOS Technology 1975
6501 - lawsuit
Mask Fixing – 30 -> 70% yield
6502 – RISC – 1mhz but instruction cycles
1975 trade show – vases of chips
Complete Product family
Kim-1
Uses PET, Apple 1 & 2, BBC Micro, Nintendo Entertainment System
Layout – crawling on tables - Visual 6502 – 3,510 transistors
Wilbur Mathys, Bill Mensch, Rodney Orgil, Ray Hirt, Chuck Peddle, Harry Bawcom, Michael Jaynes, Sydney-Anne Holt
,

## Slide 19: 6502
8-bit Commodores
Apple 1 & ][
BBC Micro
Nintendo NES
Atari 2600 (6507)
and…
Notes: cheap Microprocessor, Motorola not interested
6800 team - Peddle - joined MOS Technology 1975
6501 - lawsuit
Mask Fixing – 30 -> 70% yield
6502 – RISC – 1mhz but instruction cycles
1975 trade show – vases of chips
Complete Product family
Kim-1
Uses PET, Apple 1 & 2, BBC Micro, Nintendo Entertainment System
Layout – crawling on tables - Visual 6502 – 3,510 transistors
Wilbur Mathys, Bill Mensch, Rodney Orgil, Ray Hirt, Chuck Peddle, Harry Bawcom, Michael Jaynes, Sydney-Anne Holt
,

## Slide 20: 6502
Notes: cheap Microprocessor, Motorola not interested
6800 team - Peddle - joined MOS Technology 1975
6501 - lawsuit
Mask Fixing – 30 -> 70% yield
6502 – RISC – 1mhz but instruction cycles
1975 trade show – vases of chips
Complete Product family
Kim-1
Uses PET, Apple 1 & 2, BBC Micro, Nintendo Entertainment System
Layout – crawling on tables - Visual 6502 – 3,510 transistors
Wilbur Mathys, Bill Mensch, Rodney Orgil, Ray Hirt, Chuck Peddle, Harry Bawcom, Michael Jaynes, Sydney-Anne Holt
,

## Slide 21: 6502
8-bit Commodore
Apple 1 & ][
BBC Micro
Nintendo NES
Atari
Bender
Cyberdyne Systems Model 101
Notes: In “Fry and the Slurm Factory” – last season 1 episode

## Slide 22: 6502
Original designs lost
www.visual6502.org
6502 in action…
Notes: In “Fry and the Slurm Factory” – last season 1 episode

## Slide 23
“The 1977 Trinity”

## Slide 24
Designed by John French / Leininger
3500 units in November 1977
Z-80 CPU
4k RAM & 4k ROM - $599 (Tiny Basic)
16k RAM, 12k ROM Level II - $1099
Expansion Interface for $299, disk drive for $500
Sold 250,000 worldwide
Discontinued due to FCC interference
Many further models

## Slide 25
“The 1977 Trinity”

## Slide 26
Designed by “The Woz”, colour and sound
Introduced June 10th 1977
6502 CPU,
Colour & Expansion slots, Disk ][ Interface
4k RAM - $1298
16k RAM - $1698
600 in 1977, 7600 in 1978, 35000 in 1979
Killer app, VisiCalc